CMOP cruise plan

Oregon & Washington Coasts and Columbia River, Plume & Estuary

R/V New Horizon, cruise #NEW090512A

May 12-30, 2009

Area of Operations: Pacific Northwest coastal ocean from South Oregon to North Washington, Columbia River plume, Columbia River and its estuary

Scientific personnel

| Name | Inst | Activity | Berth | May 12-21 | May 21-30 |
| --- | --- | --- | --- | --- | --- |
| Crump, Byron | UMCES | Chief Sci., BP | 13 | morning | morning |
| Kiss, Erica | UMCES | CTD, BP, fixations | 29 | afternoon | afternoon |
| Campbell, Vikki | OHSU | CTD, DNA/RNA | 17 | afternoon | afternoon |
| Needham, David | OHSU | Primary Prod. | 20 | 0500-1700 | 0500-1700 |
| Blakely, Misty | UCSC | CTD, chemistry | 31 | morning | morning |
| Wolhowe, Matt | OSU | CTD leader | 23 | afternoon | afternoon |
| Jaramillo, Alex | OHSU | CTD leader | 25 | morning | morning |
| Durkin, Colleen | UW | CTD, help chemistry | 19 | morning | morning |
| Bender, Sara | UW | CTD, help DNA/RNA | 18 | morning | morning |
| Swalwell, Jarred | UW | CTD, Flow Cytometer | 22 | morning | - |
| Needoba, Joseph | OHSU | CDOM, Methane and NH4 oxidation | 14 | - | morning |
| Kahn, Peter | OHSU | CTD, chemistry | 24 | afternoon | - |
| Smit, Mariya | OHSU | CTD, BP, fixations | 16 | morning | - |
| Peterson, Tawnya | OHSU | CDOM, Methane and NH4 oxidation | 14 | morning | - |
| Moeller, Florian | OHSU | CTD, Methane and NH4 oxidation | 15 | - | afternoon |
| Maier, Michelle | OHSU | CTD, DNA/RNA, phytoplankton | 30 | morning | - |
| Spence, Zachary | USCG | CTD, Help with water samples | 26 | afternoon | afternoon |
| Smith, Daniel | USCG | CTD, Help with water samples | 21 | morning | morning |
| Aprans, Gus (Restech) | UCSD | Restech | 27 | morning | morning |
| BERTHS FILLED |  |  |  | 17 | 14 |
| BERTHS OPEN |  |  |  | 4 | 7 |

Watches: Morning = Midnight to Noon, Afternoon = Noon to Midnight

R/V New Horizon objectives and operations

- CTD casts and sensor-based measurements.  We will occupy a grid of stations over the Oregon and Washington continental shelf and slope to measure hydrographic (T, S, pressure), bio-optical (chlorophyll fluorescence, light transmission) and chemical (nitrate, dissolved oxygen) parameters. Combine these data with ADCP measurements of subsurface velocity to explore biophysical interactions.

- Water sampling.  We will collect water samples for DNA- and RNA-based microbial community analyses, and measure bacterial production, primary production and water chemistry across environmental gradients in pelagic environments of the Columbia River, Estuary, Plume, and along established sampling lines on the Oregon and Washington coasts.  Some sampling will be coordinated with the R/V Point Sur to sample the Estuarine Turbidity Maxima in the North and South Channels, and the Columbia River Plume.

  - Chemical and biological measurements.  Most samples will be analyzed for a suite of chemical and biological concentrations (nutrients, TDN/P, DOC, POC/N, SPM, Chl-a, HPLC pigments, cytometric cell counts, microscopic cell counts).  Select samples will be analyzed for Colored Dissolved Organic Matter (CDOM) and dissolved CH4 (at eight sites along transect from outside CRmouth, into estuary and upriver to Beaver Army Dock (BAD)).

  - Rate measurements.  Most samples will be analyzed for bacterial production rate, and select samples will be analyzed for primary production rate and for biogeochemical rate processes (CH4 oxidation and NH4 oxidation).  BP measurements will be conducted in an isotope van.  Other measurements will be incubated in on-deck incubators.

- Surface flow-through system.  We will make continuous measurements of surface water chemistry with instrumentation attached to the continuous flow seawater system.  These instruments will be ship-supplied fluorometer, flow meter, thermosalinograph, and oxygen sensor; and scientist-supplied fluorometer and flow-through cytometer.

- Dye Studies.  Conduct Dye studies to track water masses and use the SWAP system and model-based CORIE forecasts to help predict and follow coastal plume into which dye is released (coordinate with R/V Point Sur).

- Plume Feature Tracking.  Conduct Feature Tracking exercises using the SWAP system and model-based CORIE forecasts to identify sampling locations in the Columbia River Plume.  Ship will cast CTD at pre-determined locations/times to test model.

- SATURN station calibration.  Provide ground truth measurements for the SATURN biogeochemical observatory system with 24-hour CTD and water sample studies near the stations and in nearby locations.

- Estuary ETM sampling.  Sample the Estuarine Turbidity maxima in the north and south channels of the estuary with a modified CTD attached to pump tubing that is paid out during each cast (coordinate with R/V Point Sur).

We kindly request copies of all calibration/information sheets for R/V New Horizon instruments.

I. Tasks

- C.S.: Chief Scientist

- S.L.: Shift Leader – in charge when Chief Scientist is off shift.

- CTD: Run CTD casts and fill carboys from Niskin bottles for water sampling team

- Chemistry: Dissolved and particulate chemistry (nutrients and organic matter)

    - Nutrients (Nitrate plus nitrite, nitrite, ammonium, phosphate, silicic acid)

    - DOC (Dissolved organic carbon )

    - TSS (Total suspended solids)

    - POC/N (Particulate organic carbon/nitrogen)

    - TDN/TDP (Total dissolved nitrogen, total dissolved phosphorous)

    - Pigments (Chlorophyll and HPLC)

    - Methane sampling / onboard analysis (Matt Wolhowe)

- Fixations: Gluteraldehyde fixation, Flow cytometry fixation, FISH fixation

- DNA/RNA: Collect DNA and RNA samples on sterivex filters

- BP: Bacterial Production measurements in radioisotope van

- PP: Primary production (on-deck incubator)

- CH4 and NH4 oxidation experiments (on-deck incubator, Matt Wolhowe helps)

1. CTD casts and sensor-based measurements.

We will be using two types of CTD systems during the cruise.  May 12-22 we will be using a large CTD rosette carrying 24 10-L Niskin bottles (Figure 1).  This rosette will be equipped with several sensors for real-time analysis of water column conditions.  These sensors are:

- CTD, Sea-bird 911plus with pressure sensor 401K-105

- Temperature sensor, Sea-Bird SBE3Plus

- Conductivity sensor, Sea-Bird SBE4C

- Pump, Sea-Bird SBE5T

- Altimeter, Benthos 916D

- PAR sensor QSP-200L

- Fluorometer, Seapoint, 6km, Chlorophyll

- Transmissometer, WetLabs, 25cm

- Oxygen Sensor SBE43

- ISUS Nitrate sensor (supplied by scientists)

On May 22-30 we will be using a Small CTD Unit consisting of the stainless steel Sea-Bird CTD frame set in a scientist-provided metal cage.  This cage has hydrodynamic flaps to keep the CTD package from spinning in the strong currents of the estuary.  Heavy weights are attached to the bottom of the cage, and the end of a length of pump tubing is attached to the leading end of the cage.  Tubing will be clipped to the CTD wire every 3 meters during the cast.  This tubing will be removed when water samples are not required.  Most of the above-listed sensors will be attached to the inside.  See Appendix 1 for pictures of CTD cage and pump.

2.  Water sampling

| Name | May 12-21 Morning | May 12-21 Afternoon | May 21-30 Morning | May 21-30 Afternoon |
| --- | --- | --- | --- | --- |
| Crump, Byron | C.S. |  | C.S., BP |  |
| Kiss, Erica |  | CTD, BP, Fixations |  | CTD, BP, Fixations |
| Campbell, Vikki |  | CTD, DNA/RNA |  | CTD, DNA/RNA |
| Needham, David | Primary Prod. |  | Primary Prod. |  |
| Blakely, Misty | CTD, Chemistry |  | CTD, Chemistry |  |
| Wolhowe, Matt |  | CTD leader, methane |  | CTD leader, methane |
| Jaramillo, Alex | CTD leader |  | CTD leader |  |
| Durkin, Colleen | CTD, help chemistry |  | CTD, help chemistry, Flow Cytometer |  |
| Bender, Sarah | CTD, help DNA/RNA |  | CTD, DNA/RNA, Flow Cytometer |  |
| Swalwell, Jarred | CTD, Flow Cytometer |  |  |  |
| Needoba, Joseph |  |  | CDOM, Methane and NH4 oxidation |  |
| Kahn, Peter |  | CTD, Chemistry |  |  |
| Smit, Mariya | CTD, BP, Fixations |  |  |  |
| Peterson, Tawnya | CDOM, Methane and NH4 oxidation |  |  |  |
| Moeller, Florian |  |  |  | CTD, Methane and NH4 oxidation |
| Maier, Michelle | CTD, DNA/RNA, phytoplankton sampling |  |  |  |
| Aprans, Gus (Restech) | CTD |  | CTD |  |

Most water samples will be subsampled for:

DNA (OHSU)	1 sterivex, 4 ml RNAlater, Cha-seal, male luer plug

RNA (OHSU)	1 sterivex, 4 ml RNAlater, Cha-seal, male luer plug

DNA (UMCES)	2 sterivex, 2 ml DNA Extraction Buffer, Cha-seal, male luer plug

POC/N	2 ashed 25mm GF/F filters (Provided by Crump lab)

SPM	2 pre-weighed GF/F filters, labeled petri plate

Nutrients	1 nutrient bottle; Fill to shoulder (Needoba)

NH4+	1 60ml HDPE bottle, measured on board (Needoba)

TDN/TDP	1 pre-extracted 30ml bottle; add EXACTLY 20 ml of sample (provided by UMCES Horn Point Laboratory analytical services)

DOC	1 polypropylene 20ml scintillation vial; fill to shoulder

Flow cytometry	1 5ml cryo tube, 0.1ml paraformaldehyde (provided by Letelier lab)

HPLC	1 25mm GF/F filter, 2ml cryovial (provided by Letelier lab)

ChlA/phaeo	1 25mm GF/F filter, 2ml cryovial (provided by Letelier lab)

Cell counts	1 glass 7ml scint vial, 0.25ml 25% pre-filtered gluteraldehyde

BP	Bacterial production rate measured as leucine incorporation rate.

Select water samples will be subsampled for:

PP	Primary Production rate

CH4	Methane concentration

CH4 uptake	Methane uptake rate

NH4 uptake	Ammonium uptake rate

Nutrient expts.	Water incubated with nitrate, silicate, or nitrate+silicate amendments

DNA/RNA (UW)	Armbrust Lab DNA/RNA

FC	Armbrust Lab flow cytometry samples

Lugols	Armbrust Lab Lugol’s fixed seawater

PDMPO	Armbrust Lab silica staining

Fv/Fm	Armbrust Lab Photosynthetic parameters using a PhytoPAM fluorometer

BioSi	Armbrust Lab Biogenic Silica

Urea	Armbrust Lab Urea concentration

Bacteria production measurements will be carried out in an isotope van.  Other rate measurements will be set up in the wet lab and incubated in on-deck incubators plumbed with seawater (Figure 2).

3.  Surface flow-through system

The surface water flow-through system on the New Horizon is currently equipped with a flow meter, thermosalinograph, fluorometer, and oxygen sensor.  We plan to connect two devices to the surface flow-through system on the New Horizon.  The first is a dye fluorometer that will detect the dye being used for the dye studies (see below). It is a Seapoint Sensor for detecting rhodamine (http://www.seapoint.com/srf.htm ). It requires power of 8.5-20 VDC, 15mA avg., 27mA pk and outputs 0-5 VDC.  The second is a flow-through cytometer (Figure 3).  This cytometer can be loaded on the ship be two people.  It sits on a lab bench and needs about 5 feet wide by 1 foot deep of space, although it can be squeezed into 1x3.  It needs to be located somewhere near the ship’s flow through line.  We have plumbing for tee-ing into the on-board system.  We would like to plumb it as close to the flowing line as possible to minimize the dead volume.  The outflow from the cytometer is around 20 ml/min and can go into a sink or overboard.  For more information please contact Jarred Swalwell (jarred@u.washington.edu) and cc. Byron Crump (bcrump@hpl.umces.edu).

4. Dye studies

The purpose of this activity is to follow one or more plumes of dye released from the R/V Point Sur.  The R/V Point Sur will be mapping these dye plumes with a towed, undulating device.  The New Horizon will position itself near the middle of the plume based on information provided by the Point Sur.  The New Horizon will conduct a CTD cast through the dye plume every hour, and will collect water samples with Niskin bottles every six hours.  More water samples may be collected.

5. Plume Feature Tracking

The purpose of this activity is to test model predictions about salinity and temperature profiles in the Columbia River plume.  About 12 hours before we begin these exercises, we will receive coordinates and times for CTD casts from the CORIE modeling team in Portland.  We will cast the CTD every hour for ten hours at specified locations during one night-time series and again during one day-time series.  We will collect water at several stations during the daytime series with Niskin bottles.

6. SATURN station calibrations

SATURN Station calibrations requires essentially collecting data in a location that is suitable to assess the data quality of each SATURN platform (Figure 4). Water samples will be needed for nutrients, chlorophyll, CDOM, etc. RNA/DNA not necessary but could be accommodated.

7. ETM studies

Estuarine Turbidity Maxima in the North and South Channels of the estuary will be sampled during 24-hour SATURN station calibrations at SATURN01 (North Channel) and SATURN03 (South Channel).  We will cast the Small CTD unit regularly during these series, and will collect water during one ebb tide and one flood tide per station.  We are targeting:

- bottom water before ETM

- bottom water at peak ETM

- surface water at peak ETM

- bottom water after ETM

8. Columbia River Sampling

We will conduct CTD casts and collect water samples during Ebb tides on May 27-28 along a down-river transect from Beaver Army Dock to Astoria, and during a time series at a station in the South Channel of the estuary at the outlet to Cathlamet Bay, a large freshwater marsh.

The river transect sites were sampled a three depths (surface, middle, bottom) in September 2008, over the course of a minor ebb tide.  The relationship of sampling to the tides is shown in Figure 5.  On May 27th, the equivalent tidal condition occurs with a slack high tide at ~1700.  We will start sampling at Beaver Army Dock beginning ~1500 and perform a downriver transect ending off Youngs Bay ~2200.  This scheme will have to be negotiated with the Captain of the New Horizon as it involves moving during the waning light of the day.  The benefit of sampling in this manner is that it would in many ways replicate the conditions experience last September, during a period of lower river discharge.

Then beginning at ~0400 on May 28th, we will perform a time series sampling at a fixed location just off the channel leading to Saturn 4 (Mott Island Turning Basin).  That time marks slack water before the major ebb.  Anchored at that location, we will evaluate how drainage of Cathlamet Bay, a freshwater marsh, impacts the methane signature in the main Columbia River Estuary.  Sampling will be done hourly at surface, middle and bottom depths over the course of ~6hrs (until ~1000).  This period of time spans the entire major ebb.

Cruise Plan Summary

Dates / Location / CTDs # / Maximum # of water samples for biology team / Coring site #

| Date | Location† | # CTDs | Water samples | Primary Prod. | Coring+ |
| --- | --- | --- | --- | --- | --- |
| 5/11/09 | Load Ship | 0 | 0 | 0 |  |
| 5/12/09 | Newport Hydroline | 9 | 12 | 1 |  |
| 5/13/09 | Columbia River line Estuarine salinity gradient | 10 7+ | 12 7 | 1 |  |
| 5/14/09 | Dye studies (coordinated with R/V Point Sur) | 24 | 12 | 1 |  |
| 5/15/09 | Dye studies (coordinated with R/V Point Sur) | 24 | 12 | 1 |  |
| 5/16/09 | Dye studies (coordinated with R/V Point Sur) | 24 | 12 | 1 |  |
| 5/17/09 | Dye studies (coordinated with R/V Point Sur) | 24 | 12 | 1 |  |
| 5/18/09 | Dye studies (coordinated with R/V Point Sur) | 24 | 12 | 1 |  |
| 5/19/09 | Dye studies (coordinated with R/V Point Sur) | 24 | 12 | 1 |  |
| 5/20/09 | LaPush line 100m isobath CTDs | 10 8 | 12 | 1 |  |
| 5/21/09 | Dock in Astoria Plume feature tracking (spring) Nighttime | 0 10 | 0 0 | 0 0 |  |
| 5/22/09 | Plume feature tracking (spring) Daytime | 10 | 12 | 1 |  |
| 5/22/09 to 5/23/09 | SATURN-04 calibration | 25 | ? | ? |  |
| 5/23/09 to 5/24/09 | SATURN-01 calibration ETM studies North Channel (coordinated with R/V Point Sur) M. rubra sampling | 36 | ? 12 3 | ? |  |
| 5/24/09 to 5/25/09 | SATURN-03 calibration ETM studies South Channel (coordinated with R/V Point Sur) | 36 | ? 12 | ? |  |
| 5/26/09 | Dock in Astoria | 0 | 0 | 0 |  |
| 5/27/09 | River Sampling - Columbia River | 8 | 24 |  |  |
| 5/28/09 | River Sampling - Estuary | 7 | 21 |  |  |
| 5/29/09 | Open day, Transit to Newport 100m isobath CTDs | 0 8 | 0 0 | 0 0 |  |
| 5/30/09 | Dock in Newport, offload ship |  |  |  |  |
|  | Total | 313 | 154 | 10 |  |

†Station locations can be found in the Appendix

*Microbial process stations will typically collect water at 3-6 depths, 1 depth during Water Mass Tracking.

Cruise Plan Details

Times in Pacific Daylight Time (PDT)

Station sampling key:

Water samples = (w) = Several 5L Niskin bottles fired at 3 depths (unless otherwise noted) for chemistry and microbiology.

Productivity samples = (p) = Several 5L Niskin bottles fired at 2 to 6 depths at depths shallower than 60m.

Pump sampling = (pump) = Collect water with pump system attached to modified CTD.

11 May 2009

08:00	Load ship in Newport, OR. On-load radioisotope that is driven to ship from Portland, OR.

12 May 2009: Newport Hydroline

08:00 	Depart Newport for station NH-3

08:30	Safety meeting

09:00	Newport Hydroline.  CTD casts at NH-3(w), NH-5, NH-10(w,p), NH-15, NH-20(w), NH-25, NH-35, NH-45, NH-55(w).  Primary productivity samples at NH-10.  Water samples at NH-3, NH-10, NH-20 and NH-55.

19:00	Transit to CR-40

13 May 2009: Columbia River line and estuarine salinity gradient

05:00	Columbia River line.  CTD casts at CR-40(w), CR-35, CR-30(w,p), CR-25, CR-20, CR-15(w), CR-10, CR-7(w), CR-4.  Primary productivity samples as CR-30.  Water samples at CR-40, CR-30, CR-15, and CR-7.

14:30	Transit into estuary to station RM-8

15:30	South Channel.  During non-peak tides (high tide at 17:00; low tide at 22:00) sample a salinity gradient aiming to get salinity: 0, 5, 10, 15, 20 and 25 PSU. More than 6 CTDs may be required to find the correct salinities.  Start with salinity of 15 PSU.  Water samples at 6 stations at one depth each.  Also collect a freshwater sample at Beaver Army Dock.

20:00	Dock at City of Rainier dock

14 May 2009: Dye studies (coordinated with R/V Point Sur)

07:00	Transit to 1st Dye release site, Begin Dye studies.  CTD casts every hour, Water samples at 3 depths every 6 hours (06:00, 12:00, 18:00, 24:00)(middle of dye plume, within pycnocline, below pycnocline)

15 May 2009: Dye studies (coordinated with R/V Point Sur)

00:00	Continue dye Studies

16 May 2009: Dye studies (coordinated with R/V Point Sur)

00:00	Continue dye Studies

17 May 2009: Dye studies (coordinated with R/V Point Sur)

00:00	Continue dye Studies

18 May 2009: Dye studies (coordinated with R/V Point Sur)

00:00	Continue dye Studies

19 May 2009: Dye studies (coordinated with R/V Point Sur)

00:00	Continue dye Studies

20:00	Transit to LP-6.

20 May 2009: LaPush line

07:00	LaPush line. CTD casts at LP-4, LP-6(w,p), LP-9, LP-12, LP-17(w), LP-22, LP-27, LP-32(w), LP-42, and LP-52(w);. Water samples at LP-6, LP-17, LP-32, and LP-52.  Primary productivity samples at LP-6.

18:00	Transit to QRLP-a

22:00	Begin CTD casts along 100m isobath to CR-15 (QRLP-a, QR-19, GHQR-a, GH-21, WBGH-a, WB-19, CRWB-a, CR-15)

21 May 2009: Dock in Astoria, Plume feature tracking (spring)

08:00	Dock in Astoria, personnel exchange.

14:00	Transit to plume region (location to be decided)

17:00	Start Nighttime Feature Tracking (CTD casts at pre-determined sites and times). Conduct 10 CTD casts, once per hour.  No water samples.

22 May 2009: Plume feature tracking (spring), SATURN-04 calibration

04:00	Start Daytime Feature Tracking (CTD casts at pre-determined sites and times).  Conduct 10 CTD casts in Columbia River Plume region.  Water samples at 3 sites characterized by a range of surface water salinities within the plume, with 4 depths for each (surface, chl max, beneath chl max, bottom).  Primary production sample at one of the stations.

14:00	Transit to SATURN 04 site, set anchor.  Convert CTD to Small CTD Unit with heavy weights.

18:00	Begin hourly CTD casts to calibrate SATURN-04.  Test deployments with pump tubing attached during peak flood at ~22:00 in preparation for ETM sampling on May 23-25.

23 May 2009: SATURN-04 calibration, ETM studies North Channel (coordinated with R/V Point Sur)

18:00	Transit to North Channel of estuary at station NC-11, set anchor. (Note R/V Point Sur will be stationed at NC-7)

20:00	Begin hourly CTD casts.

24 May 2009: ETM studies North Channel, SATURN-01 calibration, M. rubra sampling (coordinated with R/V Point Sur)

02:00	Increase CTD casts to once every 0.5 hours. Watch for Turbidity in bottom waters.  Collect Ebb tide ETM samples (six total: bottom water before ETM, as ETM increases, peak ETM, as ETM decreases, after ETM, and surface water during peak ETM)

08:00	Increase CTD casts to once every 0.5 hours. Watch for Turbidity in bottom waters.  Collect Flood tide ETM samples (six total: bottom water before ETM, as ETM increases, peak ETM, as ETM decreases, after ETM, and surface water during peak ETM)

15:00	Detach Pump tubing.  CTD casts hourly

18:00	Transit to South Channel station SAT-03 (the SATURN-03 station).  Set Anchor on south side of channel. (Note R/V Point Sur will be stationed in middle of channel)

20:00	Begin hourly CTD casts.

25 May 2009: ETM studies South Channel (coordinated with R/V Point Sur)

02:00	Increase CTD casts to once every 0.5 hours. Watch for Turbidity in bottom waters.  Collect Ebb tide ETM samples (six total: bottom water before ETM, as ETM increases, peak ETM, as ETM decreases, after ETM, and surface water during peak ETM)

08:00	Increase CTD casts to once every 0.5 hours. Watch for Turbidity in bottom waters.  Collect Flood tide ETM samples (six total: bottom water before ETM, as ETM increases, peak ETM, as ETM decreases, after ETM, and surface water during peak ETM)

15:00	Detach Pump tubing.  CTD casts hourly

20:00	Last CTD cast

26 May 2009: Dock in Astoria

08:00	Dock in Astoria.

27 May 2009: Columbia River sampling

15:00	Sample methane along an 8-site transect from Beaver Army Dock to Young’s Bay.  Sites identified in table above.  All sampling will be done using the large CTD rosette.

28 May 2009: Columbia River sampling

04:00	Anchor near channel into Mott Island turning basin and commence sampling waters from methane as a major ebb of Cathlamet Bay occurs.  All sampling (~1hr intervals for ~6hrs) will be done using the Large CTD rosette.

29 May 2009: Open day, Transit to Newport

14:00	Transit to station CR-15.  Begin CTD casts along 100m isobath to LP-12 (CR-15, CFCR-a, CF-10, CM-10, CHCM-a, CH-10, LB-100, NH-10)

30 May 2009: Dock in Newport, offload ship.

08:00	Dock in Newport, Offload ship

Notes

-Bottom is defined in plume and coastal lines as 5 m from bottom.

-Bottom is defined in estuary (salinity gradient) as 1 m from bottom.

-Location of stations for estuary and plume will be determined the day before based on CORIE forecast.

-(w) indicates water to be collected from Niskins; bold & underline indicates microbiology cast.

-(p) indicates water is to be collected for Primary Productivity measurements.

Station Table for scheduled CTD casts

|  |  |  |  | Depth | Time at which station is complete |  | Latitude | Longitude |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Date | Station | Latitude | Longitude | m | Hour | Min |  | Deg | Min | Deg | Min |
| 12-May | Newport | 44.625 | 124.043 | 0 | 8 | 00 |  | 44 | 38 | 124 | 3 |
| 12-May | NH-3 | 44.652 | 124.130 | 48 | 8 | 48 |  | 44 | 39 | 124 | 8 |
| 12-May | NH-5 | 44.652 | 124.177 | 60 | 9 | 24 |  | 44 | 39 | 124 | 11 |
| 12-May | NH-10 | 44.652 | 124.295 | 80 | 10 | 19 |  | 44 | 39 | 124 | 18 |
| 12-May | NH-15 | 44.652 | 124.412 | 90 | 11 | 13 |  | 44 | 39 | 124 | 25 |
| 12-May | NH-20 | 44.652 | 124.528 | 140 | 12 | 09 |  | 44 | 39 | 124 | 32 |
| 12-May | NH-25 | 44.652 | 124.650 | 296 | 13 | 11 |  | 44 | 39 | 124 | 39 |
| 12-May | NH-35 | 44.652 | 124.883 | 435 | 14 | 44 |  | 44 | 39 | 124 | 53 |
| 12-May | NH-45 | 44.652 | 125.117 | 700 | 16 | 25 |  | 44 | 39 | 125 | 7 |
| 12-May | NH-55 | 44.652 | 125.367 | 2885 | 19 | 24 |  | 44 | 39 | 125 | 22 |
| 13-May | CR-40 | 46.167 | 124.910 | 969 | 5 | 44 |  | 46 | 10 | 124 | 55 |
| 13-May | CR-35 | 46.167 | 124.792 | 1097 | 7 | 12 |  | 46 | 10 | 124 | 48 |
| 13-May | CR-30 | 46.167 | 124.670 | 591 | 8 | 23 |  | 46 | 10 | 124 | 40 |
| 13-May | CR-25 | 46.167 | 124.557 | 146 | 9 | 18 |  | 46 | 10 | 124 | 33 |
| 13-May | CR-20 | 46.167 | 124.452 | 132 | 10 | 10 |  | 46 | 10 | 124 | 27 |
| 13-May | CR-15 | 46.167 | 124.333 | 110 | 11 | 04 |  | 46 | 10 | 124 | 20 |
| 13-May | CR-10 | 46.167 | 124.218 | 82 | 11 | 57 |  | 46 | 10 | 124 | 13 |
| 13-May | CR-7 | 46.167 | 124.158 | 55 | 12 | 36 |  | 46 | 10 | 124 | 9 |
| 13-May | CR-4 | 46.167 | 124.077 | 27 | 13 | 20 |  | 46 | 10 | 124 | 5 |
| 13-May | RM-4 | 46.259 | 124.013 | 30 | 14 | 18 |  | 46 | 16 | 124 | 1 |
| 13-May | RM-8 | 46.217 | 123.951 | 14 | 15 | 03 |  | 46 | 13 | 123 | 57 |
| 13-May | RM-11 | 46.193 | 123.905 | 13 | 15 | 40 |  | 46 | 12 | 123 | 54 |
| 13-May | RM-15 | 46.195 | 123.822 | 14 | 16 | 23 |  | 46 | 12 | 123 | 49 |
| 13-May | RM-23 | 46.250 | 123.677 | 14 | 17 | 25 |  | 46 | 15 | 123 | 41 |
| 13-May | Beaver | 46.182 | 123.181 | ~20 | 19 | 32 |  | 46 | 11 | 123 | 11 |
| 20-May | LP-4 | 47.917 | 124.742 | 35 | 7 | 13 |  | 47 | 55 | 124 | 44 |
| 20-May | LP-6 | 47.917 | 124.792 | 55 | 7 | 50 |  | 47 | 55 | 124 | 48 |
| 20-May | LP-9 | 47.917 | 124.875 | 82 | 8 | 35 |  | 47 | 55 | 124 | 53 |
| 20-May | LP-12 | 47.917 | 124.958 | 110 | 9 | 21 |  | 47 | 55 | 124 | 57 |
| 20-May | LP-17 | 47.917 | 125.083 | 137 | 10 | 17 |  | 47 | 55 | 125 | 5 |
| 20-May | LP-22 | 47.917 | 125.192 | 183 | 11 | 11 |  | 47 | 55 | 125 | 11 |
| 20-May | LP-27 | 47.917 | 125.308 | 494 | 12 | 17 |  | 47 | 55 | 125 | 19 |
| 20-May | LP-32 | 47.917 | 125.432 | 790 | 13 | 34 |  | 47 | 55 | 125 | 26 |
| 20-May | LP-42 | 47.917 | 125.680 | 620 | 15 | 13 |  | 47 | 55 | 125 | 41 |
| 20-May | LP-52 | 47.917 | 125.928 | 1500 | 17 | 22 |  | 47 | 55 | 125 | 56 |
| 21-May | QRLP-a | 47.725 | 124.883 | 100 | 21 | 48 |  | 47 | 44 | 124 | 53 |
| 21-May | QR-19 | 47.533 | 124.808 | 110 | 23 | 20 |  | 47 | 32 | 124 | 49 |
| 21-May | GHQR-a | 47.267 | 124.700 | 100 | 1 | 18 |  | 47 | 16 | 124 | 42 |
| 21-May | GH-21 | 47.000 | 124.695 | 110 | 3 | 13 |  | 47 | 0 | 124 | 42 |
| 21-May | WBGH-a | 46.838 | 124.595 | 100 | 4 | 38 |  | 46 | 50 | 124 | 36 |
| 21-May | WB-19 | 46.667 | 124.508 | 110 | 6 | 05 |  | 46 | 40 | 124 | 31 |
| 21-May | CRWB-a | 46.417 | 124.421 | 100 | 7 | 56 |  | 46 | 25 | 124 | 25 |
| 21-May | CR-15 | 46.167 | 124.333 | 110 | 9 | 48 |  | 46 | 10 | 124 | 20 |
| 21-May | Astoria |  |  |  |  |  |  |  |  |  |  |
| 27-May | Beaver | 46.180 | 123.180 | ~20 | 15 | 13 |  | 46 | 11 | 123 | 11 |
| 21-May | Astoria | 46.208 | 123.767 | 0 | 8 | 00 |  | 46 | 13 | 123 | 46 |
| 22-May | SAT-04 | 46.191 | 123.746 | 0 | 1 | 00 |  | 46 | 11 | 123 | 45 |
| 23-May | SAT-01 | 46.238 | 123.874 | 0 | 17 | 16 |  | 46 | 14 | 123 | 52 |
| 24-May | SAT-03 | 46.200 | 123.940 | 0 | 18 | 00 |  | 46 | 12 | 123 | 56 |
| 27-May | Beaver | 46.180 | 123.180 | ~20 | 15 | 13 |  | 46 | 11 | 123 | 11 |
| 27-May | Upriver#4 | 46.182 | 123.181 | ~20 | 15 | 58 |  | 46 | 9 | 123 | 19 |
| 27-May | Upriver#3 | 46.15 | 123.320 | ~20 | 16 | 40 |  | 46 | 13 | 123 | 25 |
| 27-May | Upriver#2 | 46.21 | 123.420 | ~20 | 17 | 25 |  | 46 | 15 | 123 | 33 |
| 27-May | Upriver#1 | 46.255 | 123.550 | ~20 | 18 | 8 |  | 46 | 14 | 123 | 41 |
| 27-May | Tongue Pt. | 46.225 | 123.680 | ~20 | 18 | 40 |  | 46 | 13 | 123 | 46 |
| 27-May | Astoria | 46.22 | 123.770 | ~20 | 19 | 6 |  | 46 | 13 | 123 | 50 |
| 27-May | Youngs Bay | 46.213 | 123.830 | ~20 | 19 | 27 |  | 46 | 12 | 123 | 52 |
| 29-May | CR-15 | 46.167 | 124.333 | 110 | 17 | 16 |  | 46 | 10 | 124 | 20 |
| 29-May | CFCR-a | 45.950 | 124.259 | 100 | 18 | 56 |  | 45 | 57 | 124 | 16 |
| 29-May | CF-10 | 45.733 | 124.185 | 110 | 20 | 36 |  | 45 | 44 | 124 | 11 |
| 29-May | CM-10 | 45.483 | 124.208 | 135 | 22 | 27 |  | 45 | 29 | 124 | 12 |
| 30-May | CHCM-a | 45.267 | 124.221 | 100 | 0 | 05 |  | 45 | 16 | 124 | 13 |
| 30-May | CH-10 | 45.050 | 124.233 | 146 | 1 | 45 |  | 45 | 3 | 124 | 14 |
| 30-May | LB-100 | 44.858 | 124.204 | 100 | 3 | 16 |  | 44 | 52 | 124 | 12 |
| 30-May | NH-10 | 44.652 | 124.295 | 80 | 4 | 53 |  | 44 | 39 | 124 | 18 |
| 30-May | Newport | 44.625 | 124.043 | 0 | 20 | 00 |  | 44 | 38 | 124 | 3 |

Berthing

01 LEVEL (UPPER DECK)

Room No.    Bunk No.

01-5        13         Chief Scientist__Byron Crump_____

01-2        14         Upper	Tawnya Peterson (1st)/ Joe Needoba (2nd)

01-2        15         Lower	Florian Moeller (2nd)

01-3        16         Upper	Mariya Smit (1st)

01-3        17         Lower 	Vikki Campbell

01-4        18         Upper	Sarah Bender

01-4        19         Lower	Colleen Durkin

01-7        30         Upper 	Michelle Maier (1st)

01-7        31         Lower 	Misty Blakely

PLATFORM DECK (LOWER DECK) STARBOARD SIDE

Room No.    Bunk No.

A1          20         Upper	David Needham

A1          21         Lower	Daniel Smith

A2          22         Upper	Jarred Swalwell

A2          23         Lower 	Matt Wolhowe

PLATFORM DECK (LOWER DECK) PORT SIDE

Room No.    Bunk No.

A8          24         Upper	Peter Kahn (1st)

A8          25         Lower	Alex Jaramillo

A10         26         Upper	Zachary Spence

A10         27         Lower	Restech: Gus Aprans

A14         28         Upper

A14         29         Lower	Kiss, Erica

CTD Cage

We constructed a cage to protect the CTD and other sensors during deployment in the Columbia River estuary.  We attach a heavy weight to help get the package below the surface currents during strong ebb tides.  The cage also has some hydrodynamic flaps to keep the package oriented properly when deployed.

Pump

We attach the ends of a rigid tube to the CTD cage and to an impeller pump on deck.  This tubing is paid out as the cage is lowered, and clipped onto the hydrowire.  Our maximum deployment depth in the estuary is approximately 25m.

Map of Job Corp dock in Astoria.  We will be docking at Peir 7 at 0800 hours on May 21 and May 26.

Map of OSU dock in Newport.  We will be departing at 0800 on May 12 and returning at 0800 on May 30.

Space allocation plan for the Wet and Dry labs.  These are tentative, mainly because your chief scientist has never seen the inside of this ship.  On loading day May 11 we will have to work together to get everyone the space they need.

# Text boxes

| New Horizon-May 2009 CH4 Sites | Lat-N | Lon-W |
| --- | --- | --- |
| Youngs Bay | 46.205 | -123.870 |
| Astoria Port Docks | 46.213 | -123.830 |
| Tongue Point | 46.220 | -123.770 |
| Upriver#1 | 46.225 | -123.680 |
| Upriver#2 | 46.255 | -123.550 |
| Upriver#3 | 46.210 | -123.420 |
| Upriver#4 | 46.150 | -123.320 |
| Beaver Army Dock | 46.180 | -123.180 |

Figure 5.  Columbia River transect for Methane sampling.  Map, stations and approximate timing during an ebb tide

Figure 1.  CTD Rosette frame for coastal and plume sampling.  Holds 24 10-L niskin bottles.

Figure 2.  On-deck incubators

Figure 3.  Flow-through cytometer.

Figure 4.  SATURN station locations